## Slide 1
Statistical Process Control
Section A.6

## Slide 2
Control Chart
Definition
A control chart for a process consists of values plotted over time used as a graphical display to detect unusual variation in a process.
A Control Chart consists of three horizontal lines:
​A Center Line that represents the average value of the quality characteristic corresponding to the in-control state.
​An upper bound called the Upper Control Limit (UCL)
​A lower bound called the Lower Control Limit (LCL)

## Slide 3
Control Chart (cont.)
Figure A6.1

## Slide 4
Control Chart (cont.)
Each point on the chart represents a sample statistic which has been calculated for the sample taken at a particular time period. The sample statistic will vary depending on the type of the control chart which is being used. If the sample statistic falls above the UCL or below the LCL, this signals unusual variation in the process and the process is deemed to be "Out of Control."

## Slide 5
The Highway Control Chart
When you are driving a car and you stay in your lane, you could say that you are operating the car "in control." The white lines that define your lane are similar to the UCL and LCL. The car would be expected to move around within the lane, which would be normal process variation. Veering outside your lane might have assignable causes such as cell phone usage, children fighting in the back seat, or any number of other distractions.

## Slide 6
Control Charts for Continuous Variables
Definition
Mean charts (-Charts) graphically display consecutive sample means with the intent of detecting a significant change in the process mean. The three methods of constructing -Charts deal with:
​-Charts where both and are known.
​-Charts using (the average of the sample ranges) to infer an estimate of the process variation.
​-Charts using the sample standard deviation to estimate the process variation.
Range charts (-Charts) graphically display consecutive sample ranges with the intent of detecting a significant change in the process variation.

## Slide 7
Control Charts for Attributes
Definition
-Charts graphically display consecutive sample proportions of defective units with the intent of detecting a significant change in the proportion of defective units which a process produces.
-Charts graphically display the number of defects per unit. An example of a unit could be a wrist watch, a hotel room, a yard of cloth, or a mile of cable. The intent is to detect changes in the number of defects per unit which a process produces.

## Slide 8
Note
If the same number of units are sampled at each time period (which, in general, they should be), the Center Line can also be calculated by finding the proportion of defective units in each sample and then averaging the sample proportions.

## Slide 9
Upper and Lower Control Limits
Definition
The Upper and Lower Control Limits (UCL and LCL) represent the boundaries between variation which is random or typical for the process and variation which is non-random or unusual for the process. These values will be calculated differently depending on the type of Control Chart being used.
​Mean Chart when and are known:
​
​
​where
​ the process mean
​ the process standard deviation
​ the number of observations in each sample.

## Slide 10
Upper and Lower Control Limits (cont.)
​Mean Chart using :
​
​
​where
​the mean of the sample ranges
​
​ a factor that relates to found in the following table.

## Slide 11
Upper and Lower Control Limits (cont.)
3 Factors for Computing Control Chart Limits |  |  | 
Sample Size | Mean Factor () | Lower Range (3) | Upper Range (4)
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  |  | 
Sample Size |  |  | 
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  |  | 

## Slide 12
Upper and Lower Control Limits (cont.)
​Mean Chart using sample standard deviation:
​
​
​where
​
​ Average of the sample standard deviations
​ critical value from the standard normal table
​ size of the sample taken at each time period.

## Slide 13
Upper and Lower Control Limits (cont.)
​-Chart:
​
​
​where
​
​ critical value from the standard normal table, and
size of the sample taken at each time period​.

## Slide 14
Upper and Lower Control Limits (cont.)
​-Chart:
​
​
​where
​
​ critical value from the standard normal table.

## Slide 15
Note
The wider the control limits the less likely we are to make a Type I Error. However, we do not want to make the control limits too wide, because then we are more likely to conclude that the process is "In Control" when it is not (i.e., make a Type II Error).

## Slide 16
Control Limits for When Standard Values of the Process Mean and Standard Deviation Are Known
Definition
where is the process mean, is the process standard deviation, and is the number of observations in each sample.

## Slide 17
Example A6.1
A manufacturing company uses a machine to punch out parts of a window hinge. Historically, the manufacturing process has produced hinges with a mean width of 0.45 inches with a process standard deviation of 0.022 inches. To monitor the production and to make sure the parts are acceptable for the next stage of home window assembly, a sample of three parts is taken each hour. The width of each part is then measured. As a result there are a total of eight samples with three observations in each sample. The table below contains the data for the widths of the hinges. Determine if the process is in control using an chart. Indicate which (if any) samples are out of control.

## Slide 18
Example A6.1 (cont.)
Sampling Data for Window Hinges (Inches) |  |  | 
Sample Number | Observation 1 | Observation 2 | Observation 3
1 | 0.42 | 0.48 | 0.46
2 | 0.44 | 0.48 | 0.45
3 | 0.44 | 0.45 | 0.41
4 | 0.47 | 0.42 | 0.46
5 | 0.53 | 0.43 | 0.42
6 | 0.47 | 0.42 | 0.45
7 | 0.44 | 0.47 | 0.50
8 | 0.48 | 0.43 | 0.44

## Slide 19
Example A6.1 (cont.)
Solution
Control limits need to be established and plotted on the chart. Typically, control limits for the chart are three standard deviations above and below the process mean for the given quality characteristic.
In this problem, we have external standards to gauge our process. In particular, the process mean (0.45) and process standard deviation (0.022) are known. Thus, the control limits are determined as follows.

## Slide 20
Example A6.1 (cont.)
Sampling Data for Window Hinges (Inches) with Sample Mean |  |  |  | 
Sample | Observation 1 | Observation 2 | Observation 3 | Sample Mean
1 | 0.42 | 0.48 | 0.46 | 0.453
2 | 0.44 | 0.48 | 0.45 | 0.457
3 | 0.44 | 0.45 | 0.41 | 0.433
4 | 0.47 | 0.42 | 0.46 | 0.450
5 | 0.53 | 0.43 | 0.42 | 0.460
6 | 0.47 | 0.42 | 0.45 | 0.447
7 | 0.44 | 0.47 | 0.50 | 0.470
8 | 0.48 | 0.43 | 0.44 | 0.450

## Slide 21
Example A6.1 (cont.)

## Slide 22
Example A6.1 (cont.)
The mean for each sample is calculated and displayed in the table above. The sample means are plotted in the figure above along with the UCL, LCL, and center line. Note that according to the chart, since all of the sample means fall within the control limits, the process is in control.

## Slide 23
Control Limits for When Standard Values of the Process Mean and Standard Deviation Are Unknown
Definition
where
the mean of the sample ranges,
the mean of the sample means, and
a factor that relates to (see Table A6.1).

## Slide 24
Example A6.2
Using the window hinge data (reproduced below) and assuming that we do not know the mean or standard deviation of the process, construct the chart for this process.

## Slide 25
Example A6.2 (cont.)
Sampling Data for Window Hinges (Inches) |  |  | 
Sample Number | Observation 1 | Observation 2 | Observation 3
1 | 0.42 | 0.48 | 0.46
2 | 0.44 | 0.48 | 0.45
3 | 0.44 | 0.45 | 0.41
4 | 0.47 | 0.42 | 0.46
5 | 0.53 | 0.43 | 0.42
6 | 0.47 | 0.42 | 0.45
7 | 0.44 | 0.47 | 0.50
8 | 0.48 | 0.43 | 0.44

## Slide 26
Example A6.2 (cont.)
Solution
In this example, we do not know the process standard deviation. However, we are going to use another measure of variation, the sample range, to compute the UCL and LCL. Since we do not know the true process mean, we are going to estimate that mean with , the mean of the sample means.
Before calculating the control limits for the chart, we need to perform some preliminary calculations. We need to calculate the mean and range for each sample. That is, the th sample mean and range are calculated as follows.
Note that is the number of observations in each sample.
The mean and range for each sample are presented in the following table.

## Slide 27
Example A6.2 (cont.)
Sampling Data for Window Hinges (Inches) with Mean and Range |  |  |  |  | 
Sample Number | Observation 1 | Observation 2 | Observation 3 | Mean | Range
1 | 0.42 | 0.48 | 0.46 | 0.453 | 0.06
2 | 0.44 | 0.48 | 0.45 | 0.457 | 0.04
3 | 0.44 | 0.45 | 0.41 | 0.433 | 0.04
4 | 0.47 | 0.42 | 0.46 | 0.450 | 0.05
5 | 0.53 | 0.43 | 0.42 | 0.460 | 0.11
6 | 0.47 | 0.42 | 0.45 | 0.447 | 0.05
7 | 0.44 | 0.47 | 0.50 | 0.470 | 0.06
8 | 0.48 | 0.43 | 0.44 | 0.450 | 0.05

## Slide 28
Example A6.2 (cont.)
Using the mean and range for each sample, we can calculate the grand mean and average range of the process. They are given by
and
Where is the number of samples.
Using the data in the above table we find the grand mean and the average range to be the following.
The table below provides factors for computing control chart limits.

## Slide 29
Example A6.2 (cont.)
3 σ Factors for Computing Control Chart Limits |  |  | 
Sample Size | Mean Factor (A) | Lower Range (D3) | Upper Range (D4)
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  |  | 
3 σ Factors for Computing Control Chart Limits |  |  | 
Sample Size | Mean Factor (A) | Lower Range (D3) | Upper Range (D4)
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  |  | 

## Slide 30
Example A6.2 (cont.)
For a sample size of 3, the mean factor, . Using a grand mean of 0.4525 and an average range of 0.0575, the control limits for the chart are determined as follows.

## Slide 31
Example A6.2 (cont.)

## Slide 32
Example A6.2 (cont.)
Examining the chart, one can see that the process mean is within the control limits. That is, each of the sample means fall within the control limits of the chart, indicating that the process is in control.

## Slide 33
3 Control Chart for the Process Range
Definition
where is the mean of the sample ranges and and are factors that can be found in the table below.

## Slide 34
Example A6.3
Using the window hinge data (reproduced below) and assuming that we do not know the mean or standard deviation of the process, construct the chart for this process.

## Slide 35
Example A6.3 (cont.)
Sampling Data for Window Hinges (Inches) |  |  | 
Sample Number | Observation 1 | Observation 2 | Observation 3
1 | 0.42 | 0.48 | 0.46
2 | 0.44 | 0.48 | 0.45
3 | 0.44 | 0.45 | 0.41
4 | 0.47 | 0.42 | 0.46
5 | 0.53 | 0.43 | 0.42
6 | 0.47 | 0.42 | 0.45
7 | 0.44 | 0.47 | 0.50
8 | 0.48 | 0.43 | 0.44

## Slide 36
Example A6.3 (cont.)
Solution
In this example, we do not know the process standard deviation. However, we are going to use another measure of variation, the sample range, to compute the UCL and LCL.
Before calculating the control limits for the chart, we need to perform some preliminary calculations. We need to calculate the range for each sample. That is, the th sample range is calculated as follows.
Note that is the number of observations in each sample.
The mean and range for each sample are presented in the table below.

## Slide 37
Example A6.3 (cont.)
Sampling Data for Window Hinges (Inches) with Mean and Range |  |  |  |  | 
Sample Number | Observation 1 | Observation 2 | Observation 3 | Mean | Range
1 | 0.42 | 0.48 | 0.46 | 0.453 | 0.06
2 | 0.44 | 0.48 | 0.45 | 0.457 | 0.04
3 | 0.44 | 0.45 | 0.41 | 0.433 | 0.04
4 | 0.47 | 0.42 | 0.46 | 0.450 | 0.05
5 | 0.53 | 0.43 | 0.42 | 0.460 | 0.11
6 | 0.47 | 0.42 | 0.45 | 0.447 | 0.05
7 | 0.44 | 0.47 | 0.50 | 0.470 | 0.06
8 | 0.48 | 0.43 | 0.44 | 0.450 | 0.05

## Slide 38
Example A6.3 (cont.)
Using the range for each sample, we can calculate the average range of the process. It is given by
where is the number of samples.
Using the data in the table we find the average range to be the following.
The table below provides factors for computing control chart limits.

## Slide 39
Example A6.3 (cont.)
3 Factors for Computing Control Chart Limits |  |  | 
Sample Size | Mean Factor () | Lower Range (3) | Upper Range (4)
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  |  | 
Sample Size |  |  | 
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  |  | 

## Slide 40
Example A6.3 (cont.)
Computing the control limits for the chart, we have

## Slide 41
Example A6.3 (cont.)

## Slide 42
Example A6.3 (cont.)
Examining the chart, one can see that the variability is within the control limits. That is, the sample ranges fall within the control limits of the chart, indicating that the process is in control.

## Slide 43
Example A6.4: Mean Charts Using
Cola Supreme has decided to use an -Chart, with an -risk of , to determine if their 15 ounce filling machine is properly adjusted. The production manager randomly selects five cans of cola and measures the amount of cola in each can. The sampling is repeated at 15 successively selected time periods.
The results are displayed below:

## Slide 44
Example A6.4: Mean Charts Using
Sample Results |  |  |  |  |  |  | 
Sample Number | Obs. 1 | Obs. 2 | Obs. 3 | Obs. 4 | Obs. 5 | Sample Mean | Sample Standard Deviation
1 | 15.00 | 14.97 | 15.01 | 15.00 | 15.04 | 15.0040 | 0.0251
2 | 14.96 | 14.98 | 14.97 | 15.00 | 14.98 | 14.9780 | 0.0148
3 | 14.98 | 14.95 | 15.02 | 14.96 | 14.98 | 14.9780 | 0.0268
4 | 15.03 | 14.98 | 14.99 | 15.00 | 15.03 | 15.0060 | 0.0230
5 | 15.01 | 14.98 | 15.04 | 14.99 | 15.05 | 15.0140 | 0.0305
6 | 14.99 | 15.01 | 15.02 | 14.98 | 15.00 | 15.0000 | 0.0158
7 | 15.03 | 15.00 | 15.04 | 14.96 | 14.97 | 15.0000 | 0.0354
8 | 15.00 | 15.00 | 15.02 | 15.00 | 15.04 | 15.0120 | 0.0179
9 | 15.00 | 15.03 | 15.01 | 14.95 | 15.01 | 15.0000 | 0.0300
10 | 14.97 | 15.01 | 14.98 | 14.96 | 15.03 | 14.9900 | 0.0292
11 | 15.05 | 15.03 | 15.00 | 14.98 | 14.96 | 15.0040 | 0.0365
12 | 15.01 | 15.00 | 14.97 | 14.96 | 14.99 | 14.9860 | 0.0207
13 | 15.02 | 14.98 | 14.97 | 14.99 | 15.03 | 14.9980 | 0.0259
14 | 14.99 | 14.99 | 14.97 | 15.00 | 14.99 | 14.9880 | 0.0110
15 | 14.95 | 15.00 | 14.95 | 15.03 | 14.96 | 14.9780 | 0.0356

## Slide 45
Example A6.4: Mean Charts Using (cont.)
​What is the Center Line of the control chart?
​What are the Upper and Lower Control Limits?
​If the given samples are taken at the next time periods, determine if each process is "In Control" or "Out of Control"?
​

## Slide 46
Example A6.4: Mean Charts Using (cont.)
Sample Number | Obs. 1 | Obs. 2 | Obs. 3 | Obs. 4 | Obs. 5 | Sample Mean
16 | 14.99 | 14.98 | 14.97 | 14.98 | 14.96 | 14.976
17 | 15.10 | 14.99 | 15.09 | 15.07 | 15.09 | 15.068
18 | 14.90 | 14.99 | 14.95 | 14.96 | 15.00 | 14.960

## Slide 47
Example A6.4: Mean Charts Using (cont.)
​Based on the control limits established, what is the probability that the production manager will conclude that the process is "Out of Control," when the process is actually "In Control"?

## Slide 48
Example A6.4: Mean Charts Using (cont.)
Solution
Step 1: Find the Center Line of the control chart.
To find the Center Line, calculate the average of the 15 sample means.

## Slide 49
Example A6.4: Mean Charts Using (cont.)

## Slide 50
Example A6.4: Mean Charts Using (cont.)
Step 2: Find the Upper and Lower Control Limits.
Since we have calculated as 14.996, to find the Upper Control Limit (UCL) and Lower Control Limit (LCL) we need both and . For , we have
.
For , the production manager wants to set the control limits such that the -risk is , thus
.

## Slide 51: Example A6.4: Mean Charts Using (cont.)
Therefore, the Upper Control Limit will be calculated as the following.
The Lower Control Limit will then be calculated as the following.

## Slide 52
Example A6.4: Mean Charts Using (cont.)
Step 3: For the given samples, state if the process is "In Control" or "Out of Control"
This step will be repeated for each additional sample. At each step, we must determine whether the process is "In Control" or "Out of Control."
Sample 16: As (i.e., the sample mean is within the control limits), the process is deemed to be "In Control."
Sample 17: As (i.e., the sample mean falls above the upper control limit), the process is deemed to be "Out of Control."
Sample 18: As (i.e., the sample mean falls below the lower control limit), the process is deemed to be "Out of Control."

## Slide 53
Example A6.4: Mean Charts Using (cont.)

## Slide 54
Example A6.4: Mean Charts Using (cont.)
Step 4: Find the probability that the production manager will conclude that the process is "Out of Control" when the process is actually "In Control".
A Type I Error is the error of concluding that the process is "Out of Control" when the process is actually "In Control."
The control limits were established such that the -risk is . Thus, by the definition of -risk, the probability of a Type I Error is 0.05.
Therefore, the probability that the production manager will conclude that the process is "Out of Control" when the process is actually "In Control" (i.e., make a Type I Error) is 0.05.

## Slide 55
Example A6.5: -Charts
Miller Manufacturing has decided to use a -Chart with 2-sigma control limits to monitor the proportion of defective circuits produced by their production process. The production manager randomly samples 100 circuits at 16 successively selected time periods and counts the number of defective circuits in the sample.
The results of the sampling are displayed below:

## Slide 56
Example A6.5: -Charts
Sample Data | 
Sample Number | # of Defects
1 | 15
2 | 10
3 | 10
4 | 11
5 | 10
6 | 9
7 | 14
8 | 11
9 | 11
10 | 14
11 | 13
12 | 14
13 | 14
14 | 10
15 | 13
16 | 13

## Slide 57
Example A6.5: -Charts (cont.)
​What is the Center Line of the control chart?
​What are the Upper and Lower Control Limits?
​During the next three time periods, 100 curcuits are sampled in each period. In the first time period 4 defective circuits are detected, 16 are detected in the second, and 12 are detected in the third. Determine if each process is "In Control" or "Out of Control"?
​Based on the control limits established, what is the probability that the production manager will conclude that the process is "Out of Control," when the process is actually "In Control"?

## Slide 58
Example A6.5: -Charts (cont.)
Solution
Step 1: Find the Center Line of the control chart.
The Center Line is calculated as follows:

## Slide 59
Example A6.5: -Charts (cont.)

## Slide 60
Example A6.5: -Charts (cont.)
Step 2: Find the Upper and Lower Control Limits.
Since we have calculate to be 0.12, to find the Upper Control Limit (UCL) and Lower Control Limit (LCL) we need both and . The production manager samples 100 units at each sample period. Thus, . Since the production manager wants to set 2-sigma control limits, and represents the number of standard deviations the control limits are set above and below the mean, .

## Slide 61: Example A6.5: -Charts (cont.)
Therefore, the Upper Control Limit will be calculated as the following.
The Lower Control Limit will then be calculated as the following.

## Slide 62
Example A6.5: -Charts (cont.)

## Slide 63
Example A6.5: -Charts (cont.)
Step 3: For the given samples, state if the process is "In Control" or "Out of Control"
This step will be repeated for each additional sample. At each step, we must determine whether the process is "In Control" or "Out of Control."
Sample 17: Since 0.04 falls below the Lower Control Limit, the process is deemed to be "Out of Control."
Sample 18: Since 0.16 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."
Sample 19: Since 0.12 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."

## Slide 64
Example A6.5: -Charts (cont.)

## Slide 65
Example A6.5: -Charts (cont.)
Step 4: Find the probability that the production manager will conclude that the process is "Out of Control" when the process is actually "In Control"?
A Type I Error is the error of concluding that the process is "Out of Control" when the process is actually "In Control."
The control limits are established with 2-sigma control limits. Thus, and the probability that the production manager will conclude that the process is "Out of Control" when the process is actually "In Control" (i.e., make a Type I Error) is 0.046. The calculation is shown below.

## Slide 66
Example A6.5: -Charts (cont.)

## Slide 67
Example A6.6: -Charts
Genuine Motors has decided to use a -Chart to monitor the number of defects per car produced by their production process. Management would like to construct the -Chart such that of the number of defects detected per car fall within the control limits, if the process is In Control. The production manager randomly samples one car at 16 successively selected time periods and counts the number of defects on the car.
The results of the sampling are displayed below:

## Slide 68
Example A6.6: -Charts
Sample Data | 
Sample Number | # of Defects
1 | 15
2 | 10
3 | 10
4 | 11
5 | 10
6 | 9
7 | 14
8 | 11
9 | 11
10 | 14
11 | 13
12 | 14
13 | 14
14 | 10
15 | 13
16 | 13

## Slide 69
Example A6.6: -Charts
​What is the Center Line of the control chart?
​What are the Upper and Lower Control Limits?
​During the next three time periods, 4 defects are detected on the first selected car, 16 defects are detected on the second, and 12 are detected on the third. Determine if each process is "In Control" or "Out of Control"?
​Based on the control limits established, what is the probability that the production manager will conclude that the process is "Out of Control," when the process is actually "In Control"?

## Slide 70
Example A6.6: -Charts
Solution
Step 1: Find the Center Line of the control chart.
The Center Line is calculated as follows:

## Slide 71
Example A6.6: -Charts (cont.)

## Slide 72
Example A6.6: -Charts (cont.)
Step 2: Find the Upper and Lower Control Limits.
Since we have calculated to be 12, to find the Upper Control Limit (UCL) and Lower Control Limit (LCL) we need both and . The control limits must be set such that of the number of defects per unit will fall within the control limits if the process is In Control. This implies that of the observations will fall outside the control limits even if the process is In Control. Given this information, the z-value is found as follows:
.

## Slide 73: Example A6.6: -Charts (cont.)
Therefore, the Upper Control Limit will be calculated as the following.
The Lower Control Limit will then be calculated as the following.

## Slide 74
Example A6.6: -Charts (cont.)

## Slide 75
Example A6.6: -Charts (cont.)
Step 3: For the given samples, state if the process is "In Control" or "Out of Control"
This step will be repeated for each additional sample. At each step, we must determine whether the process is "In Control" or "Out of Control."
Sample 17: Since 4 falls below the Lower Control Limit, the process is deemed to be "Out of Control."
Sample 18: Since 16 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."
Sample 19: Since 12 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."

## Slide 76
Example A6.6: -Charts (cont.)

## Slide 77
Example A6.6: -Charts (cont.)
Step 3: For the given samples, state if the process is "In Control" or "Out of Control"
This step will be repeated for each additional sample. At each step, we must determine whether the process is "In Control" or "Out of Control."
Sample 17: Since 4 falls below the Lower Control Limit, the process is deemed to be "Out of Control."
Sample 18: Since 16 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."
Sample 19: Since 12 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."